## Slide 1: Device Assignment in Arm CCA
Derek D. Miller
4 September 2024

## Slide 2: Introduction to Arm CCA
Arm Confidential Compute Architecture (CCA) is designed to protect data and code in use by creating isolated execution environments called Realms.
Key Features:
  Full software stack Isolation from the host OS and hypervisor
  Hardware-based security mechanisms
  Blind hypervisor – Realm can contain a full OS stack
  Support for attestation

## Slide 3: Architecture Components
RME extension in the CPU
  MMU
    Add GPC
SMMU
  Add GPC
MPE – Memory Protection Engine
  Provide encryption and optionally integrity
Completer-side PAS Filter on simple on-chip, memory mapped peripherals
Granule Protection Checks (GPC) between peripherals that can independently access memory and the system bus
  For some of these, this will be provided by the SMMU

## Slide 4: Granule Protection Check

## Slide 5: Granule Protection Check
Security state | Non-secure PAS | Secure PAS | Realm PAS | Root PAS
Non-secure | Yes | No | No | No
Secure | Yes | Yes | No | No
Realm | Yes | No | Yes | No
Root | Yes | Yes | Yes | Yes

## Slide 6: RMM
Design constraints in the RMM meant we didn’t want it to have specific drivers for multiple devices
  DA presents a standard mechanism for attesting all device types
Interrupts are directed to the CVM realm

## Slide 7: What is Device Assignment?
Definition: Device assignment allows hardware devices to be securely mapped to Realms, ensuring that only authorized Realms can access assigned devices.
Importance: Allow CCA realms’ Roots of Trust (RoT) to be extended to devices outside of the CPU
  Enabling them to use GPUs, ML Accelerators, cryptographic accelerators, even DPUs
Three broad categories of devices
  On-SoC peripherals that are not DMA-capable
    These do not need device assignment – RMM/VMM managed page tables are sufficient
  On-SoC peripherals that are DMA-capable (Root Complex Integrated Endpoints – RCiEP)
  Off-SoC peripherals
For devices with multiple interfaces, the realm must trust the device to isolate the device context appropriately

## Slide 8: On-SoC peripherals that are not DMA-capable
  Attestation is provided via the platform attestation token
  Trust in the peripheral is presumed by trust in the platform
  But the presence of the device is not explicit
    It’s implicit in the platform’s memory map

## Slide 9: On-SoC peripherals that are DMA-capable (Root Complex Integrated Endpoints – RCiEP)
Attestation is provided via the platform attestation token
  But additional GET_MEASUREMENTS calls may be supported to establish trust in the device firmware
Realm must approve it being added to its root of trust
Each device needs an EL3 driver
  The specifics of interface report retrieval is device-specific
Realm can get details on the device through the RSI_RDEV_GET_INFO call
To ensure that non-secure cannot intercede, the device should be placed behind a Realm Physical Address Space filter (by the SoC vendor)
  Limit access to Root/Realm security state

## Slide 10: Off-SoC peripherals
Device Assignment does apply
physical link must be protected against physical attacks
  By IDE or similar
Attestation is provided via TDISP/SPDM
But the realm must approve it being added
  After checking the GET_CERTIFICATES and GET_MEASUREMENTS results
Interface between the RMM and device is generic
  So the RMM does not need device drivers
  This was a requirement to keep the RMM as simple as possible

## Slide 11: Software Flow
SPDM/IDE session is setup by the RMM before the device is trusted
  Necessary to ensure integrity of certificate and measurements
Storage of certificate and measurements is done by the host
  To avoid allocations in the RMM
  RMM maintains hashes of them
Realm enters the picture relatively late

## Slide 12: Attestation challenges
Unification of Attestation “ground truth of trust”
  It is desirable to have one entity responsible for determining acceptability of a TCB
  Often, this is an external service (such as Veraison) – but essentially, attestation is establishing the suitability of an environment to a relying party
  However, RME-DA requires the Realm software to determine if it trusts the device
    It can do this autonomously (without going to an external service)
      But this separates the “ground truth of trust” between the service and the Realm software – management of this can be error prone (or, more likely, not done)
    It can do this by going to the external service
      But this adds another round trip to the external service – or the relying party
  More work needs to be done here
Inclusion of on-SOC devices in the address map means they ”appear” on the platform attestation token
  But this is not as explicit as I’d like